## Slide 1: Planning and Preparation for Extreme Precipitation Gulf of Maine Council / Working Group Meeting June 7-8, 2017
Cliff Sinnott, Executive Director
Rockingham Planning Commission - Exeter, NH
Former Chair, NH Coastal Risk and Hazards Commission

## Slide 2: Presentation
NH Coastal Risk & Hazard Commission (NHCRHC)
Extreme precipitation: NHCRHC planning assumptions
Projecting upland flooding conditions in a Lamprey (Coastal NH) Watershed
General NHCRHC Guidance about acting in uncertainty

## Slide 3: NH Coastal Risk and Hazards Commission
SB-163 Introduced by ‘Salt Water’ Senators (Watters, Stiles, Clark) in Jan. 2013
An Act… “establishing a commission to recommend legislation to prepare for projected sea level rise and other coastal and coastal watershed hazards”
Enacted July 2, 2013
Commission first assembled August 16, 2013
Ended December 1, 2016

## Slide 4: Commission Membership (= 37)
2 Senators, 2 House members
Reps from 17 coastal & tidal municipalities
State Agency designees from:
Other Stakeholders:
NHDES | NH Office of Energy & Planning
NH Fish & Game | DRED – Commissioner’s office
NHDOT | Div. of Parks and Recreation (DRED)
Bureau of Public Works | Div. of Historic Resources (DCR)
NH Homebuilders | PRIMEX
Seacoast Board of Realtors | NHMA
UNH - SeaGrant | Strafford RPC
UNH – Pres. designee | Rockingham RPC

## Slide 5: Science Advisory Panel
Established to help Commission interpret & assess peer-reviewed science
Focused on planning assumptions for:
  Sea-level rise
  Storm surge
  Precipitation
Report adopted unanimously in July 2015
Panel suggests report update at least every 2 years

## Slide 6: Precipitation
Inland areas threatened by flooding from extreme precipitation.
(Detailed assessment of precipitation trends and projections for NH in Wake et al. 2014)
Image Source: NCA (2014) – Chapter 2
Total Precipitation – Northeastern US
Observed Change: >10% Increase in mean annual precipitation in period 1895-2011.
Projected Change: Likely increase; up to 20% by 2100 compared to 2000
Extreme Precipitation – Northeastern US
Observed Change: 50% increase in the amount of precipitation falling during extreme events (largest 1% of total daily precipitation).
Projected Change: likely further increase

## Slide 7
  TP-40 Rainfall Frequency Atlas used for effective conditions = 6.3”
  Northeast Regional Climate Center Atlas for Extreme Precipitation for current conditions = 8.5”
100-year Rainfall Estimates
Notes: TP-40 (Rainfall Frequency Atlas for the US) published in 1961 used precip data from 1938-1957 (20 year time period)

## Slide 8: Extreme Precipitation Scenarios – Boston (CH2M Hill, 2013)

## Slide 9
“We are unable at present to assign with confidence future changes in extreme precipitation events. We do, however, recommend at a minimum that all related infrastructure be designed with storm volumes based on the current Northeast Regional Climate Center (Cornell) atlas to represent current precipitation conditions and infrastructure should be designed to manage a 15 % increase in extreme precipitation events after 2050 and that a review of these projections be continued.”
Extreme Precipitation - STAP

## Slide 10
PRECIPITATION:
Mean annual precipitation increase 10% from 1895-2011
Annual precipitation occurring in extreme events increased more than 50% from 1901-2012
Mean annual precipitation and precipitation in extreme events projected to increase, but magnitude is uncertain
Planning guidance:
  Use Cornell Northeast precipitation data for current projects
  Plan for 15% increase in precipitation in extreme events after 2050
  Update as new science emerges
Precipitation - Findings & Guidance

## Slide 11
Product of FEMA National Flood Ins. Program (NFIP)
Define land areas subject to periodic flooding
1% probability (100 Year Flood Zone) (“A” (flooding) & “V” zones (coastal high hazard)
0.2% probability (500 Year Flood Zone)
Towns use maps to limit building and/or define flood proofing standards to limit vulnerability (“Flood Hazard Overlay Districts”)
Property owners eligible for subsidized flood insurance
Map accuracy important to ensure those standards are applied were the threat exits
Flood Maps as planning tool
Notes: I: This project, fundamentally is about the information we (communities) use help understand flood hazards exist. The primary source of that information is FEMA FIRM maps
T: It turns out that even the information we rely on to understand flood hazards is not stable

## Slide 12
Flood Map limitations
FIRM Maps are developed from Flood Insurance Studies (FIS)
Studies use hydrologic models defined by:
  experience in regional storm event frequency and severity (the climate record)
  flooding response of the watershed (stream gauge records)
Maps are ‘backwards-looking’ and assume a static condition
The reality: both inputs are dynamic due to long term changes in storm characteristics (timing, severity, frequency) and land use change (increase in impervious surface, loss of forest, wetlands)
Notes: I: indeed there are some inherent limitations in flood maps, not because they are flowed or done poorly, but because the world they describe is changing
T: Both of these dynamic factors are acting to change flood characteristics in NH’s watersheds. The questions is, can we improve on these maps to more accurately reflect both what the risk is today and what it is likely to be 50 or 100 years in the future. In other words – by changing these maps from backwards-looking to forwards-looking; from based on an historic record to based of a projection of future conditions. This is a broader fundamental question when it come to “planning” from the legal sense, for climate change.

## Slide 13
Project Objectives:
Assess flood risk associated with combined land use and climate change scenarios out to 2100
Produce maps of the 100-year flood risk boundaries and river discharge at specific locations
Demonstrate the use of these products to support land use decision-making in coastal communities
Serve as a model for other New England watersheds
Address legal issues of using projected flood information
Assessing Flood Risk - Lamprey River Watershed
Notes: I: Enter the Lamprey River Flood Risk study…

## Slide 14
Lamprey River Watershed, New Hampshire
Notes: Orientation of the watershed
Study begins at the northern corporate limit of Raymond and ends at the Macallen Dam in Newmarket passing through five communities
Length: 33 miles (check)
Area: 211 sq. mi.
Note the RT108 corridor
The Lamprey River watershed is almost 215 square miles and consists of 15 whole or partial communities. The river is about 30 miles long with its headwaters in Northwood and releases into the Great Bay at Newmarket. 73% of the land cover within the watershed is forested, agricultural or other open space use. 13% is residential, 3% industrial/commercial and the remaining 11% is water/wetlands.

## Slide 15
Notes: I: these products will be presented in map and tabular form. Advisory Committee is help project team to define product formats that will be most helpful and useful to communities.

## Slide 16
Notes: I: So, I said there are two primary drivers changing flood behavior…lets take a look a land use first
Land use change means in this context primarily the conversion of undeveloped to developed land, but more particularly the increase in impervious surface, which increases stormwater runoff and reduced the retention time of rain on the land; and conversely, the loss of forest cover and wetlands both of which act to reduce runoff and increase the retention time of rainfall on the ground.

## Slide 17
Notes: T: Keep in mind that the flooding response of this watershed was based on conditions that existed when the study was done and before.

## Slide 18
Durham, NH
Lawrence, MA
4 Inch Precipitation Events by Decade 1948 - 2007
Notes: I: Not lets take a quick look at rain

## Slide 19
Assessing Flood Risk - Lamprey River Watershed
Notes: 14 May 2006 – Mother’s Day storm
16 April 2007 – Patriots Day storm (Nor’easter)

## Slide 20
  TP-40 Rainfall Frequency Atlas used for effective conditions = 6.3”
  Northeast Regional Climate Center Atlas for Extreme Precipitation for current conditions = 8.5”
100-year Rainfall Estimates
Notes: TP-40 (Rainfall Frequency Atlas for the US) published in 1961 used precip data from 1938-1957 (20 year time period)

## Slide 21
Lamprey River 100 Year Flood Risk Project

## Slide 22
Newmarket Effective 100 Year Floodplain

## Slide 23
Advisory Committee = municipal, regional, state, federal and non-profit representation
FEMA Region 1
USGS
NH Department of Environmental Services
NH Office of Energy and Planning
New England Interstate Water Pollution Control Comission
Lamprey River Advisory Committee
Lamprey River Watershed Association
Rockingham Planning Commission (Chair)
Strafford Regional Planning Commission
Southern New Hampshire Planning Commission
Exeter Public Works
Durham Public Works
Newmarket Planning Department
Multidisciplinary & Multijurisdictional Approach
Notes: NEIWPCC: New England Interstate water pollution control commission

## Slide 24: acting in uncertainty
UNCERTAINTY
RISK
Easy to act
Neither easy to act or ignore
Easy to ignore

## Slide 25: Guidance (for acting under uncertainty)
Incorporate ‘Risk Tolerance’ in Design.
Respond Incrementally.
Revisit and Revise.
Collaborate and Coordinate.
Make “No Regrets” Decisions.
Act Early.

## Slide 26: More Information on NHCRHC and to download report:
http://www.nhcrhc.org
(agendas, minutes, presentations, members roster, reports, resources, etc.)